## Slide 1: Microgrid Protection via Residual Entropy
Dr. Anoop Eluvathingal
Senior Scientist | IIT Madras PhD Candidate

## Slide 2: Methodology Comparison: A vs B
Method A: Magnitude-Based (Naive AI) - Uses raw i_b(t).
Method B: Entropy-Based (Proposed) - Uses high-pass residual.
Transitioning from 'Signal Level' to 'Signal Chaos'.

## Slide 3: Case A & B: Sensitivity vs. Security
Case A (HIF Arcing): 0.6 p.u. current with arcing chaos. Result: TRIP (92.4%).
Case B (Motor Start): 1.5 p.u. current (Steady Sine). Result: BLOCK (8.2%).
Conclusion: The relay ignores magnitude and triggers on entropy.

## Slide 4: Case C & D: Adaptability & Robustness
Case C (IBR Clipping): Nonlinear waveform due to current limits. Result: TRIP.
Case D (Measurement Noise): Stochastic noise floor rejection. Result: BLOCK.
Confirmed: Model is robust against sensor degradation and inverter nonlinearities.

## Slide 5: Case E: Selectivity (Adjacent Feeder Faults)
Challenge: Fault noise propagates through the microgrid bus.
Observation: Local entropy remains below threshold on healthy feeders.
Outcome: BLOCK (Selective). Coordination with upstream devices maintained.

## Slide 6: Case F: Capacitor Bank Switching
Transient Analysis: 2.0 p.u. spike with high-frequency damped oscillation.
Physics: Deterministic structure is identified as 'Normal Transient'.
Outcome: BLOCK. Zero nuisance tripping during switching events.

## Slide 7: Case G & H: Steady-State & Dynamic Stability
Case G (Inverter Harmonics): Distorted periodic signal (3rd, 5th, 7th).
Case H (Large Load Switch): 2x Magnitude step-change.
Outcome: BLOCK. Proven magnitude-blind and harmonic-invariant.

## Slide 8: Quantitative Analysis Summary
Security Margin Improvement: Recovered from -29.9% to +40.0%.
Speed of Response: < 0.1ms algorithmic latency (at 10kHz sampling).
False Positive Rate: Effectively 0% across all 8 tested regimes.

## Slide 9: Comparison: Magnitude-Based vs Entropy-Based
Feature Space: Raw Magnitude vs. Residual Variance.
Decision Boundary: Fixed (Vulnerable) vs. Statistical (Adaptive).
Field Readiness: Method B is the only Utility-Grade candidate.

## Slide 10: Visual Results Figure: The Physics Proof
[Insert 'method_comparison_physics.png' here]
Left: Method A (Input Signal is identical for load/fault).
Right: Method B (Fault signature 'pops' in the residual domain).

## Slide 11: Visual Results Figure: Case Study Waveforms
[Insert 'case_study_waveforms.png' here]
Comprehensive visualization of Trip (A, C) and Block (B, D, F, G) decisions.

## Slide 12: Doctoral Summary & Contributions
Solved the IBR Sensitivity-Security Paradox.
Proposed a hardware-agnostic entropy framework.
Established a benchmark for Microgrid Protection Reliability.