## Slide 1: Physics-Informed Hybrid Protection for IBR-Dominated Microgrids
Dr. Anoop Eluvathingal
Senior Scientist | IIT Madras PhD Candidate

## Slide 2: The Problem: IBR Current-Limiting
Inverter-Based Resources (IBRs) suppress fault current magnitudes.
Traditional ANSI 50/51 relays fail to detect High Impedance Faults (HIF).
Result: 'Invisible' faults leading to catastrophic equipment failure.

## Slide 3: Method A Failure: Magnitude Bias
Initial Model: MLP trained on raw current magnitude (ib).
Performance: 100% Sensitivity in lab, but 99.9% Nuisance Tripping in audit.
Finding: -29.9% Security Margin during normal load transients.
Conclusion: Magnitude is a false correlate for IBR protection.

## Slide 4: Method B: Residual Entropy Analysis
Innovation: Isolating Arcing Chaos from the Fundamental 50Hz Sine.
Physics: i_residual = i_total - i_rolling_mean.
Primary Features: Noise Density (Sigma) and Ripple Peak-to-Peak.
Benefit: Magnitude-invariant fault discrimination.

## Slide 5: Validation: The 8-Scenario Matrix
Sensitivity: Detected 0.6 p.u. faults (HIF Case A).
Security: Blocked 1.5 p.u. Motor Starts (Case B).
Robustness: Immune to Cap-Switching and Inverter Harmonics.
System Security Margin: Successfully recovered to >40%.

## Slide 6: Selectivity & IEC 61850 Integration
Case E: Successful discrimination of adjacent-feeder through-faults.
Communication: GOOSE-assisted coordination logic.
Result: Maximum microgrid availability during external disturbances.

## Slide 7: Implementation: Edge-AI Requirements
Hardware: ARM Cortex-M7 / TI C2000 DSP for 100μs inference.
Process: Real-time digital filtering + MLP execution.
Integration: ANSI 21LB (Load Blinder) augmented IED.

## Slide 8: Conclusion: Doctorate Readiness
Redefined protection boundaries for IBR-dominated grids.
Proven transition from Stochastic AI to Physics-Informed Logic.
Field-ready roadmap for next-gen Microgrid Protection.